## Slide 1: Stabilized Finite-Elements
Kyle Anderson
NASA Langley Research Center
Fourth High-Order CFD Workshop
June 2016

## Slide 2: Spatial Discretization
SUPG finite-element with non-diagonal stabilization
Negative Spalart-Allmaras turbulence model
  Fully coupled
  Same order as flow equations
Linear, quadratic, and cubic elements for 2D
Solution variables: density, velocity, temperature
Weak “Nitsche-type boundary conditions at wall
Forces computed from residual
Meshes generated by perturbing linear surface
Distance function using Newton algorithm not robust
Exact solution for comparison from Galbraith
All results on triangular meshes

## Slide 3: Time Advancement
Newton-based algorithm
  Step length based on realizability and line search
  Adjustable CFL number
Full linearizations
  Operator overloading
  Hand differentiation (twice as fast as OO)
GMRES
  ILU(2) preconditioning
  200-500 search directions
  Over-converge linear system 6 orders of magnitude